## Slide 1
Design and build 3D-CAD model.
Engineering simulation and analysis
Slicing and toolpath generation
Build component/Part fabrication
Post-Processing
Quality assessment and testing
DESIGN
ENGINEERING
OPERATION
SERVICE/FEEDBACK
AM - CAx Analytics
Notes: A quick reminder of the recommendations

## Slide 2
Use of information model for structuring AM-CAx information
  CAx data contain inherent useful information for the selection of process parameters for an AM build.
    CAD data: Mesh Information
    CAE data: Simulation / Analysis information
      Material information (Mechanical)
    CAM Data: Manufacturing / Process data
      Build Information
      Material information
    QC/QA data: Testing and measurement data
CAD Model
CAE Simulation and Analysis
CAM Tool / Slicing Engine
In-Situ data from AM machine
Post-Processing data
QA/QC & Testing.
  CT SCAN data
  NDT data
Datasets
Data Visualization
Machine learning techniques
Data Preparation and cleaning
Artificial Intelligence algorithms
Unified Data Model
Notes: Why are we doing this ??
This will provide us options with
explore automation of AM workflow,
defect detection,
correlation of end factors with product process variables
Enhanced process flow understanding

## Slide 3
Impact of Data Analytics
Improved decision making
Automation capabilities
Predictive modelling capability
Data Visualization
Machine learning techniques
Data Preparation and cleaning
Artificial Intelligence algorithms
Cost reduction
Achieve higher levels of customization
Improved innovation
Improved process intelligence
Significant time and resources
High error susceptibility
Proper interpretation of results
Data acquisition across domains
Advantages
Disadvantages
Data collection
Notes: A quick reminder of the recommendations

## Slide 4
Process Control in Additive Manufacturing
Process (AM)
Input
Output
In-Situ
Ex-Situ
In-Situ Process control
Ex-Situ Process control
Porosity analysis and modelling using µ-CT Scan.
3D point cloud based geometric and dimensional assessment
Melt pool monitoring sensors
Emission monitoring sensors from process
  Thermal
  Acoustic
  Electromagnetic
Notes:     General forms of process control. Why do we do this….
    Security and output control

## Slide 5
Data Analytics in AM - CAx
Data Collection
Machine Sensors
IR/Thermal Cameras
Optical Microscopes
X-ray Modules
Data Preparation and cleaning
Data Profiling
Detain and Distilling
Assess Data Quality
Documenting (metadata)
Data Delivery
Analysis/Processing Techniques and Algorithms
Machine learning techniques
Artificial Intelligence algorithms
Custom Algorithms
Data Visualization
Maps
Charts/Graphing
Tables

## Slide 6
PBF process – product variables
Control Process Variables
Laser Speed
Laser Power
Spot Size
Layer Thickness
Gas Flow Rate and Pattern
Scanning Pattern
Powder Size
Packing Density
Product Variables
Geometric Deviation
Dimensional Deviation
Strength
Hardness
Toughness
Fatigue
Residual Stress
Surface Roughness
Porosity
Other defects
Melt pool size
Monitored Process Variables
Melt pool temperature
Melt pool geometry
Residual stress build-up
Un-melted zones
Hot/cold zones
Shrinkage
Voids

## Slide 7
Data Collection from AM system
Signals from sensors embedded in the AM machine – Gas flow, build chamber, powder flow
Monitoring the powder bed and print layer
Powder bed and printed layer : geometrical distortions, powder bed inhomogeneity, levelling issues.
Sensor data
Powder bed layer scans and images

## Slide 8
Data Collection from AM system
Melt pool monitoring
Scan track / laser melting zones
Temperature distribution, melting inconsistencies, melt pool geometries.
Temperature hotspots, spatters and plume give us an idea about the interaction between laser and powder bed
Laser interaction with powder bed
Melt pool characteristics mapping

## Slide 9
Analysis Data
CT Scan Data
Part Data
Process Data
Tool Path Data
All stages of the workflow should be linked at specific points throughout the part geometry.
The 3D files from each stage of the workflow must be discretized to track changes.
Voxelization is the most suitable technique to provide geometric discretization.
Our approach: Discretisation using voxelization
This procedure allows each location on a model to be associated with the following data:
Notes:   To represent the workflow appropriately it is necessary that all stages can be linked at specific points throughout the part geometry.
  To achieve this the input files from each stage of the workflow must be discretized across the part geometry.
  Voxelization has been identified as the most suitable technique to provide geometric discretization.
    Pros and Cons: Computationally intensive, for better results smaller voxel sizes must be used

## Slide 10: Alignment
After the data is discretized from each stage of the workflow, it is aligned with respect to each other.
This will help us associate data with different stages of the workflow
1.STL Files from each stage.
2.Voxelization of each STL.
3.Conversion from voxel model to point cloud.
4.Alignment of all point clouds.
Notes:   Presence or absence of feature, proximities to edges, orientation wrt reference
  discretization of data and alignment go hand in hand. It is necessary that the voxel model from each stage of the workflow are aligned along the same orientation.
  The most suitable method of doing this is by converting each voxel model to its equivalent point cloud.
  There is significant amounts of literature available that explain how it is possible to align point clouds
  In this case a non-rigid alignment algorithm “Coherent Point Drift” is the most suitable solution.

## Slide 11: Generated unified Information Model – based on HDF5 file format.
Due to the volume of data involved the selection of the correct data management format is important.
HDF5 is a hierarchal dataset that is deemed most suitable in which to build the information model
A MATLAB script has been developed that carries out the necessary discretization and alignment tasks on all files before writing this data to a single HDF5 file.
Notes:   Once the information across the AM workflow has been discretized and aligned it can be stored.
  Due to the volume of data involved the selection of the correct data management format is important.
  HDF5 is a hierarchal dataset that is deemed most suitable in which to build the information model
  A MATLAB script has been developed that carries out the necessary discretization and alignment tasks on all files before writing this data to a single HDF5 file.

## Slide 12
Data Preparation
Defective regions of interest
Non-defective regions of interest
For efficient discovery of data pattern, it is essential to create a comprehensive and well documented dataset.
It should make use of shared and managed storage – a relational database, network file system or big data repository
The raw data must be cleaned and processed to be documented with metadata.
Deliver the data in a suitable format for the end-user with descriptive information.

## Slide 13
Analysis/Processing Techniques and Algorithms
The expected output of an algorithm will be based on whether the dataset features within a region of interest are likely to form a relationship or pattern.
Compounded learning models, filters on datasets would be required to form meaningful relationships between the data variables.
Dataset features
Learning Model / Algorithm
No defect predicted
Defect is predicted

## Slide 14
Data Visualization
Visualization of results of a test algorithm

## Slide 15
Potential Solution
Laser Power
Laser Temp.
Melt-pool Width
Scan Speed
Selection of baseline for machine and process parameters, based on previous observations on build quality.
Deviation from ideal range of parameters, could lead to an anomaly.
With further refinements, this model could be developed for active in-situ process control.

## Slide 16
Monitoring systems currently available in AM
Monitoring System | Developer | Monitor zone | Type
QM meltpool 3D | Concept Laser | Melt poot (area and intesity) | Co-axial photodiodes
QM Coating | Concept Laser | Powder bed | Off-axial camera
EOSTATE Meltpool | EOS | Melt pool | Co-axial and off-axial sensors
EOSTATE PowderBed | EOS | Powder bed | Off-axial camera
EOSTATE Exposure OT | EOS | Thermal map of powder bed | Off-axis camera
Meltpool monitoring (MPM) system | SLM Solutions | Melt pool | Co-axial pyrometer
Laser Control System (LCS) | SLM Solutions | Powder bed | Off-axial camera
MeltView | Renishaw | Melt pool | Co-axial photodiodes
LaserView | Renishaw | Powder bed | Co-axial photodiodes
 | Aconity3D | Melt pool | Co-axial photodiodes and CMOS Camera
Truprint Monitoring | Trumpf | Melt pool | Co-axial photodiodes
Truprint Monitoring | Trumpf | Powder bed and part geometry | Off-axial camera
 | SISMA | Powder bed | Off-axial camera
LayerQam | Arcam | Intensity map in a layer | Off-axial camera
Xqam | Arcam | X-ray Emissions | X-ray detector
PrintRite3D | B6 Sigma | End-to-end monitoring system | Co-axial and off-axial sensors

## Slide 17
Future steps: Structuring the data using a Standard AM Schema
A data schema is a database with a data structure, described and supported by the database management system.
Here, the data is organized in different classes according the nature and volume of data.

## Slide 18
Thank you